## Slide 1: Conflict-Aware Flight Planning for Avoiding Near Mid-Air Collisions
SASWATA PAUL
STACY PATTERSON
CARLOS A. VARELA
DEPARTMENT OF COMPUTER SCIENCE
Rensselaer Polytechnic Institute
The 38th DASC, San Diego – September 2019

## Slide 2: Motivation
The future of National Airspace System

## Slide 3: Motivation
Urban Air Mobility
  5000 aircraft in the sky at peak operational times
  Loss of standard separation increased by 10.6% in 2017
  Expected to increase with the inclusion of UAS in the NAS
Current Air Traffic Control
  Not scalable
  Centralized (518 ATC towers)
  Not formally verifiable
  Prone to human errors
Video created using images from www.flightradar24.com

## Slide 4: Motivation
Errors are catastrophic
  1st July 2002, a Tu-154 and a Boeing 757 cargo jet collided in Überlingen
    Both aircraft crashed – 69 fatalities
  29th Sept. 2006, Gol Transportes Aéreos 1907 collided with a business jet
    The Boeing 737-8EH crashed – 154 fatalities
  16th Aug. 2015, a C172 and a Sabreliner 60SC collided near San Diego
    The Cessna was destroyed – 5 fatalities
  Investigations indicated ATC error in all cases
Need for
  Decentralized, scalable, and smarter air traffic management
  Provably correct strategic conflict management

## Slide 5: Conflict-Aware Flight Planning
Goal: To create a formally-verified flight planning algorithm that can ensure standard separation between an ownship and traffic aircraft following a given set of flight-plans.
Flight-plan:
  a series of waypoints in 3D space
  a start time
  constant groundspeed and vertical speed between
  consecutive waypoints
We have used the Athena proof assistant to mechanically verify that our algorithm generates safe solutions

## Slide 6: Novelty
The solution flight-plans generated do not consist of spatial deviations
  Useful for situations where spatial deviation may be restricted by weather, airspace capacity, or restricted airspace
  Suitable for civilian use of UAS in urban environments
Formally verified to detect and resolve conflicts between entire flight-plans
Temporal dimension divided into periods of interest for conflict detection in multiple flight segments

## Slide 7: Novelty
May be used by a centralized/decentralized controller for admission control into an airspace

## Slide 8: CAFP Algorithm
INPUTS:
  A proposed flight-plan for an ownship
  A set of immutable traffic flight-plans
  A vector of discrete values of airspeed
  The horizontal wind data
Output:
  A valid flight-plan for the ownship (if possible)
    Only the groundspeed and vertical speed between waypoints is changed
    3D flight profile unchanged

## Slide 9: Conflict Between Two Flight-plans
The well-clear volume [Lee et al.]
  a cylinder of diameter D and height H around the center of the aircraft
  two aircraft are in conflict if their well-clear volumes intersect

## Slide 10: Conflict Between Two Flight-plans

## Slide 11: Conflict Between Two Flight-plans
However, this is true only under the assumption that both aircraft a and b maintain constant velocity flight between t0 and t
Flight-plans may be a sequence of multiple constant velocity flight segments
To predict conflicts between two
flight-plans, we need to discretize
the temporal dimension into
periods of interest
Notes: “Velocity” is correct here since both groundspeed and vertical speed remain constant in a flight segment

## Slide 12: Conflict Between Two Flight-plans
Period of interest - a period of time when both aircraft are known to maintain constant velocity flight
Given two flight-plans, a non-decreasing vector T of temporal points corresponding to the waypoints in each flight-plan can be computed
The period between each consecutive temporal point in T is a period of interest
Notes: Static image available on

## Slide 13: Conflict Between Multiple Flight-plans
  Input: A set of flight-plans , the horizontal and vertical thresholds D and H
  Output: FALSE if there exists a possible conflict between any Fi and Fj . TRUE otherwise.
THEOREM 4:

## Slide 14: Conflict Aware Flight-planning
The problem statement:
The strategy:
  To resolve possible conflicts between an ownship a and a traffic aircraft b, we assign suitable values of constant groundspeed between consecutive waypoints in the ownship’s flight-plan
  Given a vector of allowed airspeeds for the ownship and the wind vector , a vector of possible groundspeeds can be computed

## Slide 15: Conflict Aware Flight-planning
The strategy (contd.):
  To retain the 3D profile of the proposed flight-plan, the constant vertical speed between waypoints needs to be adjusted accordingly
  This pairwise strategy is extended to the set to find a solution such that
  Only two components of the velocity vector between waypoints are altered:
    The groundspeed
    The vertical speed
  The 3D course between waypoints remains unchanged

## Slide 16: Adjusting the Vertical Speed
The new vertical speed can be computed using the flight path angle

## Slide 17: Computing the Groundspeed Assignments
The assignment of groundspeed to the flight segments between waypoints can be arranged as an m x n matrix
  m = (number of waypoints - 1)
  n = number of possible
  groundspeeds
Initially, all cells are 0 (M0)
The cell M[r,c] is assigned a 1 if the rth segment is assigned the cth element of

## Slide 18: Computing the Groundspeed Assignments
Required properties:
  Safety Property – If a matrix is generated by the algorithm, then adding the corresponding flight-plan to the given set of traffic flight-plans must create a safe set of flight-plans
  Completeness Property – If there is a combination of groundspeeds that can create a solution flight-plan, the algorithm will not return M0.

## Slide 19: The Matrix Assignment Algorithm
The solve() function computes the solution matrix:

## Slide 20: The Matrix Assignment Algorithm
  Input: An assignment matrix , the proposed flight-plan, the set of traffic flight-plans, the vector of groundspeeds, and the thresholds D and H
  Output: Returns a complete assignment matrix if a valid solution can be found. Otherwise, returns M0
THEOREM 8:
Theorem 8 corresponds to the Safety Property

## Slide 21: The Matrix Assignment Algorithm
THEOREM 9:
Theorem 9 corresponds to the Completeness Property
Both these Theorems have been proven in Athena
* Proofs available at: http://wcl.cs.rpi.edu/pilots/fvcafp

## Slide 22: The Matrix Assignment Algorithm
The theorems in Athena :

## Slide 23: Simulations
A proof of concept implementation was developed using Python
The implementation closely followed the Athena specifications
We used D = 1 nautical miles and H = 1000 feet
All flight-plans were at a constant altitude of 5000 feet
The wind velocity used was 0 kts

## Slide 24: Simulations
First Scenario:
  F0 and F1 were in conflict and our algorithm computed a solution assignment matrix

## Slide 25: Simulations
Second Scenario:
  A third plan F2 was introduced, and our algorithm computed a solution assignment matrix

## Slide 26: Simulations
Third Scenario:
  A fourth plan F3 was introduced, but there was no possible solution, so the algorithm returned M0

## Slide 27: Simulations
Third Scenario (augmented ):
  We added a groundspeed of 60 kts to the vector of groundspeeds and a solution was found

## Slide 28: Observations
The algorithm can be effectively used to detect possible well-clear violations and compute solutions
The airspace density makes a significant impact on the availability of solutions
The range of values in also plays an important role
Since , the wind conditions can be expected to considerably influence the solution space as well

## Slide 29: Discussion
Advantages:
  Formally verified strategic conflict avoidance
  Discretizing time into periods of interest allows conflict detection and avoidance for multi-segment flight-plans
  No spatial deviation from the proposed flight-plan
  Useful in terminal STARs and urban environments which provide little room for spatial deviation (civilian applications of UAS such as package delivery)
Limitations:
  Limited solution space may not always lead to a solution
  The assumption that traffic aircraft do not deviate from their flight-plans may not always be true
  Do not consider other options – up/down/left/right/holding maneuvers

## Slide 30: Discussion
Related Work:
  Muñoz et al. - formally verified tactical collision avoidance
    Tactical avoidance does not deal with entire flight-plans
    Spatial deviation from flight path
  Balachandran et al. – used RAFT consensus for scheduling UAVs approaching an intersection
    New waypoints to maximize arrival times
  Spatial deviation may not always be possible in urban environments

## Slide 31: Concluding Remarks
The future of the NAS:
  Significant challenges in terms of air-traffic management
  ADS-B can be made a richer source of data for real-time tracking and conflict-management
  Smarter air traffic management protocols required to deal with high density of aircraft
Future directions of work:
  Algorithm that relaxes the condition that traffic flight-plans are immutable
  Cooperative protocols where all aircraft reach a mutual agreement on a single set of allowed flight-plans

## Slide 32: Questions?
Download open-source PILOTS at:
http://wcl.cs.rpi.edu/pilots
Partial support from:
Air Force Office of Scientific Research
DDDAS Program
Dr. Frederica Darema & Dr. Erik Blasch
(AFOSR Grant No. FA9550-19-1-0054, FA9550-15-1-0214, FA9550-11-1-0332),
National Science Foundation
(NSF Grant Nos. - CNS 1816307, ECCS 1462342)
MIT Press, June 2013
Consider textbook:

## Slide 33
Extra Slides

## Slide 34: Background – Cyber Physical Systems
To facilitate development of smarter flight systems, we have previously investigated:
  PILOTS (ProgrammIng Language for spatiO-Temporal data Streaming applications)
  Error detection using error signatures and error correction based on data redundancy
  Machine learning techniques to infer
    relationships from aircraft sensor data
    offline supervised training
    online prediction and learning
  Trajectory Generation for Fixed-Wing Aircraft in LOT Emergencies
    Wind-aware trajectories in the presence of constant, horizontal wind
    Possible landing options for US Airways 1549

## Slide 35: Definitions
Configuration – A vector where are the components of the position vector, is the course, is the groundspeed, and is the vertical speed of an aircraft.
State – A vector where the components of the ground-speed are
Waypoint – A vector which represents the 3D position of an aircraft in the coordinate space
Flight-plan – A vector containing a starting time and a vector of n configurations representing n waypoints

## Slide 36: Conflict Between Two Flight-plans
Given the states of two aircraft at time t0 , their 2D position and velocity vectors can be computed:
Their relative position and velocity at time t0 can be computed as:

## Slide 37: Conflict Between Two Flight-plans
Assuming that both aircraft maintain constant velocity flight, their relative position and velocity at time t >= t0 can be computed:
The well-clear volume of an aircraft is defined as a cylinder of diameter D and height H around the center of the aircraft.

## Slide 38: Conflict Between Two Flight-plans
Period of interest - a period of time when both aircraft are known to maintain constant velocity flight
Given two flight-plans, a non-decreasing vector T of temporal points corresponding to the waypoints in each flight-plan can be computed
The period between each consecutive temporal point in T is a period of interest

## Slide 39: Conflict Between Two Flight-plans
  Input: initial and final times t1 and t2 for a period of interest, two flight-plans Fa and Fb , the horizontal and vertical thresholds D and H
  Output: TRUE if there exists a time t between t1 and t2 such that there is a possible intersection of the well clear volumes. FALSE otherwise.
THEOREM 1:
Some important functions:

## Slide 40: Conflict Between Two Flight-plans
  Input: A vector of times T, two flight-plans Fa and Fb , the horizontal and vertical thresholds D and H
  Output: TRUE if there exists a possible intersection of the well clear volume between any two consecutive elements of T.
THEOREM 2:

## Slide 41: Conflict Between Two Flight-plans
  Input: Two flight-plans Fa and Fb , the horizontal and vertical thresholds D and H
  Output: TRUE if there exists a possible intersection of the well clear volume between Fa and Fb. FALSE otherwise.
THEOREM 3:

## Slide 42: Conflict Aware Flight-planning
The problem statement:
The strategy:
  Let Fb be a flight-plan in
  If Fa and Fb are in conflict, there is a time t :
  To resolve this conflict, the ground-speed between the waypoints of Fa can be changed to prevent any violations of the horizontal threshold
  Given a vector of allowed airspeeds for the ownship and the wind vector , a vector of possible ground-speeds can be computed.
  To retain the 3D profile of the proposed flight-plan, the vertical speed between waypoints need to be adjusted accordingly

## Slide 43: The Matrix Assignment Algorithm
returns TRUE iff the rth row has been assigned a 1
returns the first unassigned row of M
returns an intermediate flight-plan corresponding to the assignment matrix M
sets 1 to the cell M[r,c]
returns the index of a value in the ground-speed vector
Some more functions:

## Slide 44: The Matrix Assignment Algorithm
  Input: An assignment matrix , the proposed flight-plan, the set of traffic flight-plans, the vector of ground-speeds, and the thresholds D and H
  Output: TRUE iff the intermediate flight-plan corresponding to the assignment matrix is safe.
THEOREM 5:

## Slide 45: The Matrix Assignment Algorithm
  Input: An assignment matrix
  Output: TRUE iff all the rows have been assigned a ground-speed.
THEOREM 6:

## Slide 46: The Matrix Assignment Algorithm
  Input: A value of ground-speed, an assignment matrix , the proposed flight-plan, the set of traffic flight-plans, the vector of ground-speeds, and the thresholds D and H
  Output: TRUE iff the value can be safely assigned to the first unassigned row of the assignment matrix.
THEOREM 7:

## Slide 47: Dynamic Data Driven Avionics
Our Goal: To create a dynamic data driven trajectory generation system to assist pilots in such situations by taking into consideration dynamic aspects such as partial power, wind, etc.
Our model uses geometric criteria for generating trajectories using different bank angles and corresponding radii of turn and glide ratios for different drag configurations.
Our aircraft model is parameterized on a Baseline Glide Ratio for clean aircraft configuration assuming best gliding airspeed in straight flight.
We dynamically infer the baseline glide ratio to update our model in order to accurately reflect the current performance of the aircraft.

## Slide 48: Simulations

## Slide 49: Dynamic Data Driven Model
Fig: Dynamic Data Driven Flight Trajectory
Generation
Fig: Damaged Aircraft Model

## Slide 50: Low-altitude trajectories
For a given runway and a given bank angle, we have two scenarios:
  Low Altitude scenario:
  In this case, the trajectory consists of a simple Dubins Airplane Path that brings the aircraft to the runway.

## Slide 51: High-altitude trajectories
  High Altitude scenario:
  When a simple Dubins Airplane Path brings the aircraft too high above the runway.
  We find an intermediate point to lose excess altitude by extending the final approach along the runway heading.
  In this case, the trajectory consists of:
    A simple Dubins Airplane Path to bring the aircraft over the runway
    An integral [0,1,2….] number of spiral turns to lose excess altitude
    An Extended Runway of length X ∈ [0, 2πR g/g0 ) if integral number of turns cannot bring the aircraft down to the runway at proper altitude.
    A landing configuration glide ratio and airspeed is assumed for the extended runway segment.

## Slide 52: High-altitude trajectories
High Altitude Scenario where number of spirals > 0

## Slide 53: High-altitude trajectories
High Altitude Scenario where number of spirals = 0

## Slide 54: Extended Runway Segment
We use a dirty (landing) configuration glide ratio in the extended runway segment to make sure that the starting point of this segment is at an altitude from which the aircraft can make it safely to the runway.

## Slide 55: Trajectory Safety Metrics
We introduce safety metrics to evaluate trajectories.
Evaluation of trajectories makes it possible for a pilot to make a better informed choice in a shorter time.
The Metrics are:
  Average altitude
  Average distance from runway
  Average bank angle over height
    measures the occurrence of steep turns near the ground
  Total time
  Extended final runway segment distance
  Number of turns

## Slide 56: Trajectory Safety Metrics
Each metric is normalized relative to the minimum or maximum (whichever is desired) and then evaluated in our safety metric equation
We introduce an Utility Function computed by taking a weighted average of all the metrics
This Utility Function is then used to rank the trajectories generated according to their – higher value of utility function implies better trajectory and a better rank
The utility function can be easily modified to account for other factors like Wind

## Slide 57: Effect of Wind on Trajectories
Wind has a profound impact on the shape of flown trajectories with respect to the ground.
Effect of wind on straight flight Effect of wind on turns

## Slide 58: Effect of Wind on Trajectories
In the presence of wind, turns have ground-tracks that are trochoidal rather than circular.
Straight line flights create ground-tracks that are different (have a crab angle).

## Slide 59: Effect of Wind on Trajectories
Therefore, in the presence of wind the ground-tracks may be significantly altered, taking an aircraft away from the intended runway.
Wind also affects ground-speed -- a tail-wind can increase ground-speed while a head-wind can decrease it; thereby affecting the effective gliding range of a gliding aircraft.
A trajectory generated without considering wind may become invalid in the presence of wind
Therefore, wind has to be considered in the generation phase itself

## Slide 60: Effect of Wind on Trajectories
Parts of a typical trajectory
Our typical trajectory has 5 unique segments
Each segment is affected by wind in a different way

## Slide 61: Effect of Wind on Trajectories
Effect of a 40 knot wind from different directions

## Slide 62: Effect of Wind on Trajectories
Effect of a West-wind of different magnitudes

## Slide 63: Generating Wind-Aware Trajectories
We define the following:
An air trajectory is a trajectory flown with respect to the moving airmass
The corresponding ground trajectory is the 3D projection with respect to the ground frame of reference
A no-wind air trajectory is not corrected for wind and might take an aircraft away from the target runway
A wind-aware air trajectory is corrected for wind so that it can lead an aircraft to a runway in the presence of wind

## Slide 64: Generating Wind-Aware Trajectories
A wind-aware trajectory is a trajectory to a virtual runway, the ground trajectory of which can bring an aircraft to the position of the actual target runway, in the 3D space.
The virtual runway is a point lying in the upwind direction from the target runway.

## Slide 65: Generating Wind-Aware Trajectories
In the presence of horizontal wind, the effective baseline glide ratio (ge) with respect to the ground is different from the aerodynamic baseline glide ratio (g0).
However, the rate of descent remains unaffected by horizontal wind as it has no vertical component.

## Slide 66: Generating Wind-Aware Trajectories
Two conditions need to be met by a valid wind-aware trajectory:
The trajectory must be able to bring the aircraft down to the altitude of the runway.
The end of the trajectory must meet the coordinates of the runway in the two-dimensional space.

## Slide 67: Generating Wind-Aware Trajectories
Therefore, in order to compute valid trajectories, we make the following assumptions:
The aircraft always flies with the best gliding airspeed v.
For each segment in an air trajectory, time t is required to fly that segment with respect to the airmass.
The aircraft follows each segment of the air trajectory for time t.

## Slide 68: Generating Wind-Aware Trajectories
Assumptions 1, 2 and 3 imply that a ground trajectory will lose exactly the same amount of altitude as the corresponding air trajectory since time in air is equal – ensuring Condition I.
The problem is thus reduced to finding a virtual runway such that Condition II holds true.

## Slide 69: Generating Wind-Aware Trajectories
We propose an analytical solution for calculating the virtual runway for trajectories where the Dubins path segment is of the form Right-Straight-Right or Left-Straight-Left.
We also propose a heuristic iterative solution for cases that are not covered by our analytical formula.
We were able to generate wind-aware trajectories in under 50 milliseconds on an Intel Core i7-7500U CPU - 2.70GHz.

## Slide 70: Generating Wind-Aware Trajectories
Heuristic iterative algorithm.

## Slide 71: Generating Wind-Aware Trajectories
Wind-aware trajectory from 5000 feet in 40 knots West-wind
Wind-aware trajectory from 5000 feet in 40 knots West-wind

## Slide 72: Generating Wind-Aware Trajectories
Wind-aware trajectory from 8000 feet in 40 knots West-wind

## Slide 73: Generating Wind-Aware Trajectories
Wind-aware trajectory from 10000 feet in 40 knots West-wind

## Slide 74: Generating Wind-Aware Trajectories
We successfully generated a wind-aware trajectory to LGA31 from an altitude of 3850 feet, assisted by a 30 knots North-wind, even though a no-wind trajectory in the same configuration was not possible.

## Slide 75: Discussion
With a proper wind model, it is possible to design prediction based dynamic data-driven systems that can generate wind-aware 3D trajectories in the event of a loss-of-thrust scenario.
Trajectories generated are of the highest fidelity since they take into consideration the capabilities of the damaged aircraft and the prevailing wind conditions during an actual emergency.
It allows us to compute wind-assisted trajectories when no-wind trajectories are not possible.
Considering wind in the trajectory generation phase itself may present new wind-assisted options or reject options rendered infeasible by wind.